IPv6
Computer networks
Seminar 6

---
IPv6 address space
- IPv6 address size is 128 bits (RFC 4291)
  - space: 2^128 addresses
- Like IPv4 is divided to the network address and host address
  - Usually with mask /64
- IANA address ranges released
  - 2000::/3 Global Unicast	[RFC4291]
  - FC00::/7 Unique Local Unicast	[RFC4193]
  - FE80::/10 Link Local Unicast	[RFC4291]
  - FF00::/8 Multicast	[RFC4291]

---
IPv6 address notation
- Full notation
  - eight groups of four hexadecimal digits separated by colon „:“
    - 2001:0000:0db8:0000:0000:0000:1428:57ab
- Short notation
  - Four zeros in a group can be written as one zero
    - 2001:0:0db8:0:0:0:1428:57ab
  - One or any number of consecutive groups of 0 value may be replaced with two colons
    - 2001:0:0db8::1428:57ab
    - It is not possible: 2001::0db8::1428:57ab
      - ambiguous

---
IPv6 address assignment methods
- Manually configured
- IPv6 autoconfiguration based on known network prefix and MAC address of NIC (ICMPv6)
- using DHCPv6
- Manual configuration
  - administratively difficult
  - long addresses are mistake-prone

---
IPv6 Autoconfiguration
- Easier configuration of IPv6 on local network
- Address derived from advertised network prefix and from NIC MAC address
- Required the presence of the device which is able to provide necessary ICMPv6 messages
  - ICMPv6 server
  - stateless configuration
  - Potentially dangerous
    - Every connected client is able to derived the address

---
Address plan and network topology
It is required to ensure
appropriate routing in the network
Host chooses local address itself within assigned subnet

---
IPv6 configuration on Cisco router
- Enabling routing process
  - (config)#ipv6 unicast-routing
- IPv6 configuration on interface
  - (config)#interface <type><num>
  - (config-if)#ipv6 address <ipv6>/<mask>
  - (config-if)#no shutdown

---
Switched module for routers
The module provides more (typically 4 or 8) Ethernet switched ports (fast or gigabit Ethernet)
- We need to use VLANs to configure these ports
  - (config)# interface gi0/1/0
  - (config-if)# switchport mode access
  - (config-if)# switchport access vlan 123
  - (config-if)# no shutdown
- The created virtual interfaces for VLANs are then configured as normal interfaces
  - (config)# interface vlan 123
  - (config-if)# ip/ipv6 address …
- We can check the interfaces in normal way:
  - # show ip interface brief
  - # show interface vlan 123

---
IPv6 configuration in Linux
- Iproute2 usage
  - Assigning IPv6 address to interface
    - ip addr add <ipv6>/<mask> dev <dev>
  - Removing IPv6 address from interface
    - ip addr del <ipv6>/<mask> dev <dev>
  - Removing all configured IP addresses from interface
    - ip addr flush <dev>
  - Default gateway configuration
    - ip route add default via <ipv6_gw>

---
Configuration example in Linux
- Removing addresses from int. eth0
  - ip addr flush eth0
    - ip a f eth0
- Setting the address 2001:2345::0120/64 on eth0
  - ip addr add 2001:2345::0120/64 dev eth0
    - ip a a 2001:2345::0120/64 dev eth0
- IPv6 default gateway configuration
  - ip route add default via 2001:2345::0001
    - Ip r a default via 2001:2345::0001

---
Static routing
- IPv6 static routing
  - (config)#ipv6 route <ipv6_net>/<mask> <next_hop>
  - It is necessary to add routes leading to not connected parts of network topology on routers
  - Every router has 3 static routes

---
IPv6 autoconfiguration
- Configuration of Ipv6 network prefix propagation from router
  - (config)#interface <type><num>
  - (config-if)#ipv6 nd prefix <IPv6_pref>/<mask>
- Setting sending interval of router advertisements
  - (config-if)#ipv6 nd ra-interval <num_sec>
- Generating IPv6 address on computer
  - ip link set <dev> down
  - ip link set <dev> up

---
Configuration checking
- Device accessibility
  - ping6 <IPv6_addr>
- Path to the device from L3 view
  - traceroute6 <IPv6_addr>
  - tracepath6 <IPv6_addr>